## Slide 1: Antenna design update, April 15
John Cumner, Quentin Gueuning

## Slide 2: Elliptical dipole
~10dB backwards, beams uniformity deteriorates at ~100MHz
Impedances for a range of diameters:
1600/1400mm
1050/1330mm (Farfields shown)
1000/800mm
Farfields broadly similar, some increased smoothness for smaller dipoles
10m ground plane
Cumner

## Slide 3: Elliptical dipole
PROs | CONs
Simple design | Requires ground plane
Flat input impedance | Requires balun
Low input impedance | Beam separates at top end of frequency band
Possible to expand to second polarization | 
Cumner

## Slide 4: Flat log spiral
10-20dB backwards. Closer beam uniformity, although rotational features can be seen.
Quite a resonant impedance, this is from the size of the antenna.
Impedance about ~120Ω
Cumner

## Slide 5: Flat log spiral
PROs | CONs
Wide sky beam | Requires ground plane
Covers full band | Requires balun
Relatively low input impedance | Beam rotates with frequency
 | Spiky input impedance
Could be designed without,
have not yet looked into it
Cumner

## Slide 6: SARAS2 monopole
Taken from Singh et al 2017 https://arxiv.org/pdf/1710.01101.pdf
Is designed to function higher than our frequency
band, would need to be scaled up.
Possible -30dB S11m, and uniform farfields
Cumner

## Slide 7: SARAS2 monopole, style
PROs | CONs
Monopole, so no balun | Needs scaling to our band
Uniform farfields | Unpolarized
Match-able input impedance (at higher frequencies) | 
Low feedpoint | 
Cumner

## Slide 8: Conical log spiral
D>~
-20/30 dB backward -> better than a ground plane
Constant across all band
Gueuning

## Slide 9: Conical log spiral
PROs | CONs
Very low beam chromaticity | Matching circuit
No ground plane | 1 pol
Flat input impedance | Few meters high
Wire version (simple) | 
Cover all band | 
lossless broadband tapered matching circuit along the apex of the cone (e.g. coax to parallel wire transformer)
RF system on the ground inside the spiral ?
Gueuning

## Slide 10: Helical antenna
Monopole mode Travelling wave mode
(D<< ) (D~
-20 dB backward
20-30% bandwidth
A lot of power is diffracted toward ground ! + small bandwidth
Gueuning

## Slide 11
Helical antenna (traveling wave mode)
PROs | CONs
Smaller ground plane (directive antenna) | Bandwidth (S11=-15 dB) max 25-30 %
Input impedance potentially tunable down to 50 Ohm | 1 pol
Pencil beam | 
Gueuning

## Slide 12: Cavity-backed flat spiral
The cavity destroy the frequency independent property of the spiral
Gueuning

## Slide 13: Additional designs
Sinuous antenna
Inverted Vivaldi feed, possibly with shielding
Horn antenna
HIBiscus antenna (https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=8072391)